Control Logic

For Site Ambient

Low Temperature Conditions.

Each compressor aftercooler section includes a temperature measuring device that senses the metal temperature of the cooler header box. The temperature measuring device is wired into it’s respective compressor control panel where it is relayed via communication link to the station control panel. The station control panel will monitor all three temperatures as permissives. If two of the three permissives are below the temperature setpoint the station control panel will lock out activation of the station suction and discharge header block valves and an alarm warning will be displayed on the screen. If two of the three temperature devices are at or above the setpoint activation of the station suction and discharge header block valves will be allowed by the station control panel.

SECTION 15

MAINTENANCE

Safe Maintenance Practices

Blinding & De-blinding procedure

The word blinding in following paragraphs means blinding, deblinding, blanking, deblanking, spading, despading, disconnecting or similar terms. Line breaking precautions should be followed prior to the additional precautions described below.

Operations & Mechanical personnel shall ensure use of correct rating and size of blind

Handle(tail) of a blind shall be distinctively identifiable from handle of a spacer or orifice plate

Other Utility Lines: (Plant Air, Instrument Air, Nitrogen line, Water lines including Sea Water). All utility lines shall be considered as hydrocarbon contaminated. Gas tests shall be conducted during spreading of the flange and precautions & procedures determined accordingly

Double Block & Bleed: Some high pressure or hazardous content lines are provided with two block valves separated by a spool piece that has a bleed connection vented to a safe location. Any passing material will be vented instead of reaching the danger end

Unions: Inserting a disc between union faces is not considered as positive isolation. Union shall be disconnected and capped/plugged at the danger end.

Blinds that were in position for a long time should be removed and inspected before being used as positive isolation.